## Slide 1
More CT Stuff
Ge Wang
AI-based X-ray Imaging System (AXIS) Lab
Rensselaer Polytechnic Institute, Troy, New York, USA
Oct. 8, 2021

## Slide 2: MI Schedule for F21
Tue | Topic | Fri | Topic
08/31 | Introduction | 09/03 | Neuron, Network & Backpropagation
09/07 | No Class | 09/10 | Hands-on 1: Python, Colab, & TensorF
09/14 | Architectures & Training | 09/19 | Hands-on 2: MNIST Classification
09/21 | Image Quality I | 09/24 | CT Physics
09/28 | CT Reconstruction | 10/01 | Deep CT Reconstruction
10/05 | Hands-on 3: CT Networks | 10/08 | More CT Contents
10/12 | MRI Physics | 10/15 | Spin-Echo
10/19 | K-Space Theorem | 10/22 | More MRI Contents
10/26 | Mid Exam | 10/29 | Deep MRI Reconstruction
11/02 | Hands-on 4: MRI Networks | 11/05 | Nuclear Physics
11/09 | Nuclear Imaging | 11/12 | US Imaging
11/16 | Optical Imaging | 11/19 | Multimodality Imaging
11/23 | Hands-on 5: Image Conversion | 11/26 | Thanksgiving
11/30 | Image Quality II | 12/03 | Stability, Interpretability, & Others
12/07 | Overview | 12/10 | Final Exam
Office Hour: Teaching Day 5-6pm: https://rensselaer.webex.com/meet/wangg6

## Slide 3: Half-scan Angular Range

## Slide 4: Is Full-scan (360˚) Necessary?

## Slide 5: What Is the Min Angular Range?

## Slide 6: Equi-spatial Fan-beam Formula
Wang, Lin, Cheng: IEEE TIP 2:543-547, 1993

## Slide 7: Where Error Is?

## Slide 8: Cone-beam Scanning
β
α
General Scanning Trajectory

## Slide 9: Obliqueness Correction
Obliqueness Correction in Fan-beam Formula
Obliqueness Correction in Cone-beam Formula
An X-ray Hits the 2D Detector Plate Obliquely, Determined by Two Angles

## Slide 10: Outline
Spiral CT – Longitudinal Data Truncation
General Idea
Approximate & Exact Image Reconstruction
Interior Tomography – Transverse Data Truncation
General Idea
Main Merits

## Slide 11: Spiral Cone-beam CT
Wang, G, Lin, TH, Cheng PC, Shinozaki DM, Kim HG: Scanning cone-beam reconstruction algorithms for x-ray microtomography. Proc. SPIE 1556:99-112, July 1991
Wang G, Lin TH, Cheng PC, Shinozaki DM: A general cone-beam reconstruction algorithm. IEEE Trans. on Med. Imaging 12:486-496, 1993

## Slide 13: Impact of Spiral Cone-beam Scanning
There are ~200M Multi-slice/Cone-beam CT Scans Annually, a Majority of Which are in the Spiral/Helical Cone-beam/Multi-slice Mode
To solve the long-object problem, a first level of improvement with respect to the 2D FBP algorithms was obtained by backprojecting the data in 3D, along the actual measurement rays. The prototype of this approach is the algorithm of Wang et al.
Defrise, Noo, Kudo: A solution to the long-object problem in helical cone-beam tomography. Phys. Med. Biol. 45:623-643, 2000
Many advances in cone-beam reconstruction have been made recently thanks to the quest for an attractive reconstruction method in helical cone-beam tomography.
Pack, Noo, Clackdoyle: Cone-beam reconstruction using the backprojection of locally filtered projections. IEEE Trans. Medical Imaging 24:1-16, 2005

## Slide 14: Data Sufficiency in 3D
At least a point on a source orbit on any plane in an object

## Slide 15: Tam Window & PI-Line (Necessity)
A PI-Segment is a line segment with its endpoints on one helical turn. Every point is on one and only one PI-line (you can try to prove!).
The helical portion between the two endpoints of a PI-Segment is called a PI-arc.
Tam window is defined as the detector area on a cylindrical surface delimited by two consecutive helical turns (also called the Tam-Danielsson Window).
PI-Segment
Tam-Window

## Slide 16: Perfect Mosaic (Global Involvement)
To compute planar integrals, Grangeat’s algorithm requires that the cone-beam data is not truncated
To employ Grangeat’s algorithm for spiral cone-beam CT, a perfect mosaic scheme is designed to compute planar integrals
Oblique Plane Cutting through a Long Object
Seamless Coverage with Divergent X-rays

## Slide 17: Exact Spiral Cone-beam CT
Detector
Plate
Source
Object
Pi-Line
Katsevich A: An improved exact filtered backprojection algorithm for spiral computed tomography. Advances in Applied Math. 32: 681-697, 2004

## Slide 18: Triple-source Spiral Cone-beam CT
Zhao, J, Jin YN, Lv Y, Wang G: A filtered backprojection algorithm for triple-source helical cone-beam CT. IEEE Trans. Med. Imaging 28:384-393, 2008
Lv Y, Katsevich A, Zhao J, Yu HY, Wang G: Fast exact/quasi-exact FBP algorithms for triple-source helical cone-beam CT. IEEE Trans. Med. Imaging 29:756-770, 2010

## Slide 22: Ge’s PhD Dissertation 30 Years Ago

## Slide 24: Outline
Spiral CT – Longitudinal Data Truncation
General Idea
Approximate & Exact Image Reconstruction
Interior Tomography – Transverse Data Truncation
General Idea
Main Merits

## Slide 25: Interior Problem
Interior Problem Is to Perform Image Reconstruction over an Interior Region of Interest (ROI) from Transversely Truncated Data in an Exact Fashion.
Ueda et al.: https://doi.org/10.1117/12.2255706

## Slide 26: Solution Non-uniqueness
According to page 169 of Natterer’s book, there are many non-trivial ghost functions in the interior ROI.
A ghost function does not affect the measured interior scan data at all.
The variation of the ghost is small well inside the ROI but it increases rapidly towards the boundary of the ROI, and not bounded.
Hence, theoretically exact image reconstruction over the ROI is simply impossible in an unconstrained functional space.

## Slide 27: Two Conclusions (Heuristic but Misleading!)
From the “particle” (pixel/voxel) point of view, we have to peel an onion from outermost to inner most. In this process, each measurement carries unique information (line integral and planar integrals in the 2D and 3D cases respectively). Only when outer shells are determined, we can estimate pixel/voxel values of inner shells. Hence, “outer” data are needed for interior reconstruction.
From the “wave” (Fourier analysis) point of view, all the measurement data are collected to fill in the Fourier space and are necessary since you do need all the Fourier spectral components to perform the inverse Fourier transform that is to reconstruct an underlying image. Any data truncation will compromise some Fourier components adversely, and globally affect the quality of a reconstructed image.

## Slide 28: Interior Tomography
Object
Wide Beam
Source
Trajectory
ROI
Narrow Beam
Trajectory
Regular Reconstruction
Interior Problem
ROI
Known
Sub-region
ROI
Sparsity
Model
Landmark-based
Interior Tomography
Sparsity-based
Interior Tomography

## Slide 29: Interior Reconstruction
Global Reconstruction from Complete Projections
Ground Truth ROIs
from Global Reconstruction
Interior Reconstruction from Truncated Projection

## Slide 30: Merits of Interior Tomography
Less Is Deeper
Less Is Larger
Less Is Faster
Less Is Less
Less Is More

## Slide 31: Less Is Deeper
Use of less projection data for accurate image reconstruction demands deeper insight, more advanced theory and more powerful tools.

## Slide 32: Computed Tomography (Wholesale)
t
θ
Sinogram
X-rays
Projection: Linear integrals
t
θ
y
x
π
Measurement
Reconstruction
Object

## Slide 33: Inner Vision with Local Data (Retail)
t
θ
Sinogram
X-rays
Projection: Linear integrals
t
θ
y
x
π
Measurement
Reconstruction
Object
X
X

## Slide 34: Less Is Larger
Acquisition of less projection data is achieved with a narrower beam, and an object larger than the beam width is not a concern.

## Slide 35: Big Patient Problem

## Slide 36: Less Is Faster
Less data means smaller detector size, faster frame rate, and more imaging chains, all of which contribute to an accelerated data acquisition process.

## Slide 37: Multi-source Interior Tomography
Ye YB, Yu HY, Wei YC, Wang G. International Journal of Biomedical Imaging, Article ID:63634, 2007
Wang G, Yu H, Ye Y. Medical Physics. 36:3575-3581, 2009
Wang G, Yu H, Ye YB. Virginia Tech Patent Disclosure on May 15, 2007, US Patent Application 12/362,979 allowed on October 21, 2009
Detector
Source

## Slide 38: Less Is Less
Less data is equivalent to less radiation dose, because of not only a narrower beam but also a more relaxed angular sampling requirement in the longitudinal studies or multi-scale scenarios.

## Slide 39: Less Is More
Use of less data is advantageous in more modalities beyond CT, such as other straight-ray tomographic techniques and even in small-angle curvilinear geometry, and more applications of various types. Furthermore, less data means more recon/training time!

## Slide 41: SMART Imager
x
y
o
Detector
Source
Detector
Source
Stationary Multi-source AI-powered Real-time Tomography (SMART)
#Wu WW, #Tang YH, Lv TL, Niu C, Wang C, Guo YY, Chang YC, *Wang G, *Xi Y: Stationary Multi-source AI-powered Real-time Tomography (SMART) for Dynamic Cardiac Imaging. ArXiv, 2021

## Slide 42: Sparsity Promotion + Deep Image Prior
Output
Image
Noisy Input
U-Net Module
#Wu WW, #Tang YH, Lv TL, Niu C, Wang C, Guo YY, Chang YC, *Wang G, *Xi Y: Stationary Multi-source AI-powered Real-time Tomography (SMART) for Dynamic Cardiac Imaging. ArXiv, 2021

## Slide 43: Deep Image Prior
Dmitry Ulyanov, Andrea Vedaldi, Victor Lempitsky
Partial content of this slide refers the presentation given by Dmitry Ulyanov regarding to the paper

## Slide 44: Architecture used in the experiments

## Slide 45: Image restoration - Method
– Clean image
– Corrupted/degraded image (observed)
- Restored image
Degradation for denoising:
Restoration Model:
If there is no preference for prior, the prior will be a constant. Then,
  => the best estimation of the clean image is the corrupted image
likelihood prior

## Slide 46
– Clean image
– Corrupted image (observed)
- Restored image
  Expressed as energy minimization problem:
where is a task-dependent data term, is a regularizer
For example:

## Slide 47: Deep Image Prior
– Corrupted image (observed)
Parametrization:
Interpreting the neural network as a parametrization
In particular, most of their experiments are performed using a U-Net type “hourglass” architecture(also known as “decoder-encoder”) with skip-connections, where z and x have the same spatial size.
Convolutional network with parameter 
Fixed input z

## Slide 48: Deep Image Prior step by step
– Corrupted image (observed)
- Restored image
1. initialize z
  For example, fill it with uniform noise U(-1, 1)
2. Solve
  With any favorite gradient-based method
3.Get the solution

## Slide 49: Inpainting Text inpainting

## Slide 50: Image restoration
sampled to drop 50% of pixels at random
g is the result from comparison with Shepard networks

## Slide 51: Homework
Finishing reading Chapter 3 of the textbook by Paul
Understand the derivation steps (Eqs. (1) – (10)) in the 1st cone-beam spiral/helical CT paper (approximate spiral cone-beam reconstruction): https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=241876, and explain the derivation in your own words in a tutorial-like report (see the following slides as hints)

## Slide 53: Geometric Relationship
X-ray source on the s-axis
Arbitrary Point (Impulse)

## Slide 54: Differential Contribution